## Slide 1
RIIHAN201E: Operate a Forklift
RIIHAN201E — Operate a forklift
ACME Skills Institute
Notes: Welcome everyone. My name is [Trainer Name]. Before we begin, let's cover some housekeeping: please note the location of amenities and emergency exits. Please switch your phones to silent. This course will provide you with the skills and knowledge to operate a forklift safely and effectively. We'll cover planning, pre-operational checks, safe operation, and shutdown procedures. Your assessment will involve a written knowledge test and a practical demonstration. Let's get started.

## Slide 2
Session 1 — Preparing for Operations
Understand work requirements and documentation
Identify and control hazards
Select correct PPE
Understand forklift attachments and capacities
Communicate with others on site
Notes: This first session is all about preparation. A safe lift starts long before you turn the key. We'll cover how to plan your work, identify risks, and ensure you have the right gear for the job. Proper planning prevents poor performance and, more importantly, accidents. (Covers Element 1). Timing: ~5 mins.

## Slide 3
Planning the Job
Accessing job documentation
Interpreting work orders and plans
Confirming requirements with supervisors
Understanding site rules and procedures
Applying for necessary permits
ACME Skills Institute
RIIHAN201E
Notes: First, you need to understand the task. This means reviewing documents like work orders, Safe Work Method Statements (SWMS), or site plans. Always clarify any confusing instructions with your supervisor before you start. Ask the group: 'Why is it crucial to confirm instructions before you start?' This ensures you, your supervisor, and your colleagues all have the same understanding of the task. (Covers 1.1, 1.2, PE7, FS1). Timing: ~10 mins.

## Slide 4
Hazard Identification and Control
Spotting potential hazards (e.g., pedestrians, obstacles)
Assessing risks (likelihood and consequence)
Using the hierarchy of control
Implementing control measures
Considering environmental issues (spills, noise)
ACME Skills Institute
RIIHAN201E
Notes: A hazard is anything with the potential to cause harm. A risk is the likelihood of that harm occurring. We use the hierarchy of control to manage risks. From most to least effective, it's: Elimination, Substitution, Engineering controls, Administrative controls, and finally, PPE. We must also consider our impact on the environment, like preventing spills or minimising noise. (Covers 1.3, KE1). Timing: ~15 mins.

## Slide 5
Personal Protective Equipment (PPE)
Why PPE is the last line of defence
Selecting the right PPE for the task
Common forklift operator PPE
Checking PPE is in good condition
Wearing and storing PPE correctly
ACME Skills Institute
RIIHAN201E
Notes: PPE is your last line of defence, used when other controls can't eliminate the risk. For forklift operations, this typically includes high-visibility clothing and steel-capped boots. Your site's policies will dictate the specific requirements. Always inspect your PPE for damage before use and store it correctly. (Covers 1.4, PE8, KE1). Timing: ~10 mins.

## Slide 6
Forklift Attachments and Capacity
Identifying approved attachments
Understanding the data plate/load chart
How attachments affect stability and capacity
Complying with operating capacities
Never use unapproved or damaged attachments
ACME Skills Institute
RIIHAN201E
Notes: Every forklift has a data plate, or load chart, that tells you its maximum lifting capacity at different load centres. Adding an attachment like fork slippers or a jib will change—usually reduce—that capacity. You must understand how to read the plate and account for any attachments to prevent overloading, which can lead to tipping. (Covers 1.5, PE6, KE3, FS2). Timing: ~15 mins.

## Slide 7
Site Communication
Coordinating with other workers and plant
Using two-way radios
Understanding hand signals
Maintaining eye contact with spotters
Reporting your movements clearly
ACME Skills Institute
RIIHAN201E
Notes: Clear communication is vital for safety. You need to coordinate your movements with pedestrians, other vehicle operators, and spotters. This can be done using two-way radios, horns, and standard hand signals. Always make positive eye contact to confirm signals are understood. Let's practice a few common hand signals now. (Covers 1.6, PE14). Timing: ~10 mins.

## Slide 8
Check Your Understanding
KNOWLEDGE CHECK
Where do you find the forklift's lifting capacity?
What is the first step in the hierarchy of control?
Name two common hazards in a forklift operating area.
Why must you communicate with others on site?
ACME Skills Institute
RIIHAN201E
Notes: Let's quickly review. Ask questions to the group. Expected answers: 1. On the data plate or load chart. 2. Elimination—removing the hazard completely. 3. Pedestrians, blind corners, uneven surfaces, overhead obstructions. 4. To ensure everyone's safety and to coordinate work activities efficiently. (Covers E1). Timing: ~5 mins.

## Slide 9
Session 2 — Safe Forklift Operation
Conducting pre-start and post-op checks
Operating the forklift safely
Lifting, moving, and placing loads
Monitoring the work area
Parking and shutting down correctly
Notes: Now we move into the practical side of things. This session covers the complete operational cycle, from the moment you approach the machine to when you park it at the end of your shift. We will focus on the techniques and awareness needed to operate safely and efficiently. (Covers Element 2). Timing: ~5 mins.

## Slide 10
Pre-Start Checks
Using a pre-start checklist
Visual inspection (tyres, forks, mast, guards)
Checking fluid levels (oil, fuel, coolant)
Testing controls, horn, and lights
Reporting any faults found
ACME Skills Institute
RIIHAN201E
Notes: Every shift must begin with a thorough pre-start check using a checklist. This involves a walk-around visual inspection, checking fluids, and testing all functions like brakes, steering, and warning devices. If you find any fault, the machine must be tagged out of service and the issue reported immediately. Never operate a faulty forklift. (Covers 2.1, 2.2, PE2, PE11, KE3). Timing: ~15 mins.

## Slide 11
Operating the Forklift
Correct start-up and warm-up procedure
Maintaining 3 points of contact
Smooth and controlled movements
Understanding the stability triangle
Keeping forks low when travelling
No passengers allowed!
ACME Skills Institute
RIIHAN201E
Notes: When getting on or off, always maintain three points of contact. Operate all controls smoothly—no jerky movements. A key concept is the 'stability triangle'; keeping the combined centre of gravity within this triangle prevents tipping. When travelling, keep the load low and tilted back. And remember, forklifts are designed for one person only—the operator. (Covers 2.4, PE3, KE3). Timing: ~15 mins.

## Slide 12
Practical: Pre-Start Check
ACTIVITY
In small groups, get a pre-start checklist.
Go to the assigned forklift.
Conduct a full pre-start check.
Identify and document any 'faults' planted by me.
Report your findings back to the group.
ACME Skills Institute
RIIHAN201E
Notes: Time to put theory into practice. I'll divide you into small groups. Each group will get a checklist and be assigned a forklift. I've placed some minor, safe 'faults' on each machine. Your job is to find them, document them correctly on the checklist, and explain what the proper procedure would be. I will be supervising at all times. (Covers 2.1, 2.2, PE2, PE11). Timing: ~25 mins.

## Slide 13
Handling Loads Safely
Assessing the load (weight, size, stability)
Positioning the forks correctly
Lifting the load smoothly
Tilting the mast back for travel
Placing the load securely
Using attachments correctly
ACME Skills Institute
RIIHAN201E
Notes: Before lifting, assess the load. Is it stable? Is it within your forklift's capacity? Approach the load squarely and ensure forks are spread wide and fully inserted. Lift, then tilt back. When placing the load, ensure it's stable and secure before backing away. We'll also cover the correct procedures for fitting and removing attachments. (Covers 2.3, 2.4, 2.6, PE4, PE6). Timing: ~20 mins.

## Slide 14
Monitoring Your Environment
Constantly scanning the work area
Anticipating traffic flow
Choosing the safest, most efficient route
Watching for pedestrians and other vehicles
Responding to alarms and warning systems
Maintaining a safe following distance
ACME Skills Institute
RIIHAN201E
Notes: Situational awareness is critical. You must constantly be scanning your surroundings—looking for pedestrians, other vehicles, and potential hazards. Use your horn at intersections and blind corners. Listen for any warning alarms from your machine and know what they mean. Always choose the safest route, even if it's not the shortest. (Covers 2.5, 2.7, 2.8, PE9, PE10, PE12). Timing: ~15 mins.

## Slide 15
Parking and Shutdown
Parking in designated, safe areas
Lowering the forks to the ground
Applying the park brake
Neutralising controls
Turning off the engine and removing the key
Conducting a post-operational inspection
ACME Skills Institute
RIIHAN201E
Notes: The shutdown procedure is just as important as the pre-start. Park on level ground in a designated area, away from traffic. Lower the forks fully to the ground to prevent a trip hazard. Apply the park brake, put the controls in neutral, turn off the engine, and remove the key. Finally, do a quick post-op inspection to check for any damage that occurred during your shift. (Covers 2.9, PE2, PE5). Timing: ~10 mins.

## Slide 16
Check Your Understanding
KNOWLEDGE CHECK
How high should your forks be when travelling with a load?
What is the 'stability triangle'?
What should you do if you find a fault during a pre-start check?
List three steps of the shutdown procedure.
ACME Skills Institute
RIIHAN201E
Notes: Time for another quick check. Ask questions to the group. Expected answers: 1. As low as possible while clearing the ground (approx. 150mm), with the mast tilted back. 2. The area between the front wheels and the rear axle pivot point that contains the forklift's centre of gravity. 3. Do not operate it. Tag it out of service and report it according to workplace procedures. 4. Any three of: Park on level ground, lower forks, apply park brake, neutralise controls, turn off engine, remove key. (Covers E2). Timing: ~5 mins.

## Slide 17
Session 3 — Post-Operational Activities
Maintaining a clean and safe work area
Managing and reporting hazards
Completing required documentation
Reviewing key course concepts
Notes: Welcome to our final session. The job isn't finished when you turn the engine off. This session covers the essential wrap-up activities: housekeeping, hazard reporting, and paperwork. These steps ensure the work area is safe for the next person and that there's a clear record of your work. (Covers Element 3). Timing: ~5 mins.

## Slide 18
Housekeeping
Why good housekeeping is important for safety
Clearing the work area of debris
Disposing of waste correctly (e.g., pallets, shrink wrap)
Recycling materials where possible
Storing equipment and materials properly
ACME Skills Institute
RIIHAN201E
Notes: A tidy workplace is a safe workplace. Good housekeeping reduces trip hazards, fire risks, and allows for efficient movement of people and plant. At the end of your task, clear away any rubbish like broken pallets or plastic wrap, and dispose of it according to your site's procedures. (Covers 3.1, KE1). Timing: ~10 mins.

## Slide 19
Reporting and Documentation
Reporting any new hazards identified
Completing pre-start checklists
Filling out logbooks or shift reports
Recording maintenance issues
Filing documents as per workplace procedures
ACME Skills Institute
RIIHAN201E
Notes: Accurate records are a legal requirement and a key part of a safe workplace. This includes your completed pre-start checklist, a logbook of operations, and any fault or hazard reports. Ensure your writing is clear and you file the documents in the correct place so others can access them. (Covers 3.2, 3.3, PE13). Timing: ~10 mins.

## Slide 20
Activity: Scenario Debrief
ACTIVITY
Read the provided work scenario.
Identify the potential hazards.
Describe the steps you would take from start to finish.
What documentation would you need to complete?
Discuss your plan with your group.
ACME Skills Institute
RIIHAN201E
Notes: Let's bring it all together. I'm giving each group a short work scenario. Your task is to plan the job from start to finish, considering everything we've learned: hazard identification, controls, communication, safe operation, and documentation. After 15 minutes, we'll come back together and each group will present their plan. (Covers all Elements). Timing: ~20 mins.

## Slide 21
Course Summary and Next Steps
Plan every job: check docs, assess risks, use PPE.
Always do your pre-start and post-op checks.
Operate smoothly and be aware of your surroundings.
Handle loads within the forklift's capacity.
Keep the site tidy and complete your paperwork.
Next step: Practical assessment.
ACME Skills Institute
RIIHAN201E
Notes: That brings us to the end of the training. We've covered planning, checking, operating, and cleaning up. The key message is to always think about safety first. The next step is your assessment, which will include a knowledge test and a practical demonstration where you'll operate the forklift to complete a work task. I'll now explain the assessment process in detail. Are there any final questions? (Covers all Elements, PE, KE, Assessment Conditions). Timing: ~10 mins.